## Slide 1
Version Control Recommendations
June 2014
Vivado Design Suite
Notes: This presentation covers key recommendations in Vivado 2014.1 for customers.

## Slide 2: General Revision Control Philosophy
Designed to be “Friendly” to Revision Control
  But we do not have direct integration with specific tools
  Generally Prefer ASCII-based internal files (xml project files)
  Tolerate read-only sources “locked” in revision control
  Tolerate hidden “dot” files inserted by version control tools
  Minimize file updates on opening projects and only write changes
Work with Different Use Models
  IDE vs non-GUI
  Project vs non-project
  Distributed vs Centralized Revision Control Tools
We do not recommend revision control on “active” projects
  Separate “sources” outside projects works best
  You save off a project – but easy to corrupt projects if you don’t get all files

## Slide 3: Helpers for Revision Control
Tcl script to recreate a project
  Write_project_tcl creates a “template” that you can use/modify
IP Integrator has write_bd_tcl
  Creates a tcl script to recreate just the bd
  Highly version dependent – like the ip
  Doesn’t currently work w/ remote sources
Make files with Tcl scripts
  Reproduce the project given input sources
Diff/Merge Tools from Revision control
  Scripts to recursively check in/out directories
  Diff versions and staged changes
  Report changes between versions
  Back out and revert committed changes

## Slide 4: Revision Control Improvements in 2014.1
Files needed to recreate the project
  All source files remote to the project
  XPR file only (recreates all the project files from remote sources)
  IP Integrator Block Design (.BD from standalone directory)
  IP from the IP Catalog (.XCI)
  System Generator projects (.SLX)
Issues addressed in IP Integrator
  AXI Interconnect instance names are now preserved
  XCI files not changed on disk until BD is saved
Notes: We have not drastically changed our revision control recommendations. We still recommend users place “source” files in directories outside the active project. These source files include HDL, constraints, and other input files. This also includes IP from the Manage IP project which is pointed to by the xci file, as well as IPI subsystems created in remote directories. Tcl scripts are generally used to recreate the project from these sources which are placed under revision control. If these sources are fully generated (IP and IPI sources), even if they are “read only” under revision control – the project or projectless flows can faithfully reproduce the design, with some minor gaps that we are still working on (ipi bds with saved text and locations are not yet saved in the .bd – a separate ascii file would be required to reproduce those customizations). We still do not recommend placing active projects directly under revision control – nor do we advocate partially checking in generated target files from IP or IPI subsystems.
What is new in 2014.1 is now revision control users are able to use just the XPR project file without all the project directory structure to recreate the project from the remote sources to reproduce the project without creating/managing a Tcl script to recreate the project. The xpr project file can be used “standalone” – much like an ip .xci file can be used to reproduce all the generated output products. The .bd still requires all the .xci files beneath it – and this is why we are still advocating IPI subsystems to be placed in a separate directory – and all files under that directory put in revision control – after the IPI system is stable and not changing (much).
Vivado now also has support for fully generated read-only sources.
IP Integrator has changed in three ways to make using revision control easier:
When running “Validate Design” and the AXI Interconnect is updated, the instance and file names do not change
When IP parameters are changed, the BD on disk is not changed until changes are saved
Deleting an IP and closing the BD without saving changes with not affect the design

## Slide 5: Project with Sources Under Revision Control
project_1.xpr
project_1.srcs
project_1.data
project_1.runs
project_1.ioplanning
constrs_1
sources_1
project_1.cache
sim_1
Remote Sources
HDL (Verilog/VHDL)
IPI BD (entire dir)
IP XCI (entire dir)
Sys Gen SLX (entire dir)
XDC Constraints
Tcl Scripts
Sim Testbenches
COE/BMM/ELF

## Slide 6: IP Under Revision Control
Use Standalone Manage IP
  Put the IP outside the project to be checked into revision control
  Choose a directory – normally at same level as working project
Check in the directory next to the managed_ip_project folder
  And everything below it (.xci, .dcp, .veo, . xmlall subdirectories
Instantiate by adding .xci file as remote source
  Make sure “copy into project” option is not selected
  Must be fully generated, preferrably w/ dcp

## Slide 7: IP Integrator Under Revision Control
Create the block diagram in a remote directory
  Just like IP, and make sure it is fully generated
  Iterate until happy w/ BD
Check in entire directory
  And all subdirectories
Add .bd as a remote source in top project
  Read only is fine for implementation
  Must be fully generated

## Slide 8: System Generator Under Revision Control
Build System Generator in a Standalone directory
  Like IP – separated from project
  Currently doesn’t support OOC
Check it into revision control, like IP
  Entire directory, including subdirs
Add .slx to top project
  It will be copied into the project, and generated
  Matlab license required (otherwise add the dcp remote)

## Slide 9: Version Control File Life Cycle
stage files
checkout
Git Rep.
Staged
Modified
Ignored
Files
Tracked Files
Unmodified
commit
edit files
add
remove

## Slide 10: Working with Source Files (Git as an Example) – 1/2
Set Up New Repository in existing directory
  Initialize git (creates .git subirectory):
  Start Tracking file changes:
  Create your initial “snapshot”:
Use the latest snapshot (possibly making local changes)
git init
git add *.v
git add *.vhd
find . –name “*” | xargs git add
git commit –m “Initial project version”
git clone \\full_path_to_master\myProject.git

## Slide 11: Working with Source Files (Git as an Example) – 2/2
Staging
  Query
  Discard any local changes and revert to last commit
  Report differences between staged and last commit
  Removing files from version tracking
  Ignore tracking (add files to ignore to .gitignore)
Branching and Merging
  Advanced workflows possible – following software design models
git status
git checkout
git diff
git rm foo.tcl
cat .gitignore

## Slide 12: Lab 1
Set up a new project with “ThreeFlop” RTL and XDC
Create a Makefile to call vivado with 2 targets:
  Setup creates a project with remote sources
  Clean – deletes everything except the Makefile
Use Git Commands to check in all sources, the Makefile, scripts
  git init
  git add
  git commit –m “initial project checkin”

## Slide 13: Lab 2
Create a Managed IP project for AXI_IIC
Using a script fully generate the IP with OOC flow
Check it into revision control
Iterate and change a customization option

## Slide 14: Lab 3
Create a Block diagram system with remote BD
Use write_bd_tcl