## Slide 1
June 2015
Using Revision Control with Vivado

## Slide 2
Overview of revision control (10 min)
Recommendations for Vivado (20 min)
Lab exercise using Git and Make (80 min)
Summary / Next Steps / Q&A (10 min)
Agenda

## Slide 3: Why use revision control?
Automates critical management of development
  Milestones are “backed up”
  Can revert to previous milestone if necessary
  Changes are logged
Reduces compile times
  Dependency tracking – only build when inputs change
  Take advantage of parallelization – independent steps can run in parallel
Most customers use some form of revision control
The UltraFast Design Methodology Guide (UG949) recommends using revision control with Vivado Design Suite
Notes: The parallelization benefit comes from following the recommended methodology for revision control. This methodology focuses on dependency management, leverages bottom up design and allows the launching of OOC runs in parallel. There will be no runtime required to update things that don’t need to be updated.

## Slide 4: Which revision control systems do you use?
Notes: Here are 12 examples of revision control systems. This is not a comprehensive list.

## Slide 5: Vivado revision control philosophy
Designed to be “friendly” to revision control
  No direct integration with specific tools
  Generally prefer ASCII-based internal files (XML project files)
  Tolerate hidden “dot” files and read-only sources “locked” in revision control
  Minimize file updates on opening projects and only write changes
Work with different use models
  GUI (IDE) vs non-GUI (TCL scripting)
  Project vs non-project flows
  Distributed vs centralized revision control repositories
Notes: It is clear that Vivado can’t be integrated with all of the revision control systems that customers may want to use. Therefore, Xilinx has a philosophy for Vivado Design Suite to make it as easy as possible for the customer to use Vivado with the revision control system of their choice.
Note that sources files are ASCII – even for data files. COE, BMM, etc are all ASCII.

## Slide 6: Recent improvements in Vivado
2015.1
  Only the .bd file is required to recreate a block design
  Compared to 2014.1 the average number of files per IP is about 1/3
  Increased / focused testing around recommended methodology
Updates to Chapter 2 in the UltraFast DMG coming June 8th!
Updated Revision Control Quick Take Video coming soon!
New Lunch and Learn coming soon!
2015.3
  Introduction of core container – one file per IP
  Reduction of side files required by IP Integrator
  Further reduction in the number of files per IP
  New revision control tutorial available via DocNav

## Slide 7: Two documented revision control strategies
Chart: Revision Control Strategies
| 2 | 0.4
Flexibility | 2.7 | 0.8
Maximum Flexibility
  Option to use IP in future releases of Vivado without upgrading
  Shorter runtime to rebuild project
Minimum Files
  The least number of files to manage at the expense of flexibility and run time
Xilinx recommendation

## Slide 8: Overview of recommended directory structure
Manage different source types in separate remote directories
Use a “work” directory to compile the design and to create Vivado projects
Set up the Vivado project with remote sources from the various directories
  Elect to not copy them into the project
Either manage revisions from the remote sources area directly or use it as a local sandbox for the project

## Slide 9: Project with sources under revision control
project_1.xpr
project_1.srcs
project_1.data
project_1.runs
constrs_1
sources_1
project_1.cache
sim_1
Remote Sources
HDL (Verilog/VHDL)
IPI BD (entire dir)
IP XCI (entire dir)
Sys Gen IP XCI (entire dir)
XDC Constraints
Tcl Scripts
Simulation Testbenches
COE/BMM/ELF
Notes: From a high level, this is how it would look. Only the items inside the gold clouds are managed by the revision control system.

## Slide 10: Maximum flexibility - Recommended files to manage
If using projects, manage just the .xpr file or the Tcl recreate script
  Use the write_project_tcl command to create a script to re-create the project
  Do not check in the project sub-directories
Use your own judgment on directory structures for RTL, XDC, etc.
For IP and IP Integrator sources, manage the entire directory tree
  Generated sources can be used in future Vivado releases
Notes: Going down one level of abstraction deeper, this is how it would look with the recommended flow that allows maximum flexibility.
The primary recommendation is to use TCL otherwise use the XPR. Make sure to test the XPR to make sure data is not missed and to check relative paths.

## Slide 11: Maximum flexibility - Recommended files to manage
Manage Vivado HLS source files, scripts, example projects, and packaged IP
Manage the entire System Generator directory for DSP sources
Manage Scripts and Docs as desired
For SDK, manage the .hdf file
Notes: Manage any handoff files.

## Slide 12: Minimum files - Recommended files to manage
If using projects, manage just the .xpr file or the Tcl recreate script
  Use the write_project_tcl command to create a script to re-create the project
  Do not check in the project sub-directories
For IP, check in the .xci file only
  The .xci file can be used recreate the IP output products
  IP can only be recreated using the version of Vivado the IP was created with
For IP Integrator, check in the .BD file or the Tcl recreate script
  Use the write_bd_tcl command to create a script for the block design
Notes: Note that some IP have side files – Block Memory Generator, SysMon and FIR Compiler, for example.

## Slide 13: Minimum files – Recommended files to manage
Manage Vivado HLS source files, scripts, example projects, and packaged IP
Manage the entire System Generator directory for DSP sources
Manage Scripts and Docs as desired
For SDK, manage the .hdf file

## Slide 14: Knowledge check
What should be checked into a revision control system?
  BD
  IP
  Constraints
  Project directories
  Verilog sources
  VHDL sources
  All of the above
Which of the two documented approaches to revision control is the preferred approach that Xilinx recommends?
  Maximum flexibility or Minimum files

## Slide 15: Best practices for revision control
Create a Tcl script to recreate a project
  Write_project_tcl creates a “template” that you can use/modify
IP Integrator has write_bd_tcl
  Creates a Tcl script to recreate just the bd
  Highly version dependent – like the IP
Script check-in / check-out flow
Notes: Diff/merge tools from revision control
  Scripts to recursively check in/out directories
  Diff versions and staged changes
  Report changes between versions
  Back out and revert committed changes

## Slide 16
Git and Make Primer

## Slide 17: Git file life cycle
stage files
checkout
Git Rep.
Staged
Modified
Ignored
Files
Tracked Files
Unmodified
commit
edit files
add
remove

## Slide 18: Working with source files in Git
To set up a new repository in an existing directory
  Initialize git (creates .git subirectory):
  Start tracking file changes:
  Create your initial “snapshot”:
Use the latest snapshot (possibly making local changes)
git init
git add *.v
git add *.vhd
find . –name “*” | xargs git add
git commit –m “Initial project version”
git clone \\full_path_to_master\myProject.git

## Slide 19: Working with source files in Git
Staging
  Query
  Discard any local changes and revert to last commit
  Report differences between staged and last commit
  Removing files from version tracking
  Ignore tracking (add files to ignore to .gitignore)
Branching and Merging
  Advanced workflows possible – following software design models
git status
git checkout
git diff
git rm foo.tcl
cat .gitignore

## Slide 20: Make – A brief primer on dependency management
Make is an open source tool to build things from source files
  Takes a “makefile” which describes how to build:
    Inputs to a compilation step
    Commands to execute
    Order of operations when there are multiple steps
    Steps that don’t need to be run are skipped (based on files and timestamps)
    Targets/dependencies are usually files on disk – commands generate files
Makefile structure
  target: dependencies …
    commands
    …
Documentation:
  http://www.gnu.org/software/make/manual/html_node/index.html
This is a Tab Character – don’t forget it!

## Slide 21: Standard conventions with Make
Calling “make” with a specific target – generates just that target
Calling “make” with no arguments – runs the first target
First target is “all”
  Builds everything in the project
  “All” is a phony target (no file on disk)
  Dependencies are all the inputs (and outputs of intermediate steps)
Last target is “clean”
  Deletes everything in the project dir (except Makefile)
  Always start clean

## Slide 22
Lab Exercise
80 Minutes
Using Git and Make with Vivado

## Slide 23: Lab overview
This 80 minute lab exercise is broken down into 6 main sections
Simple RTL project creation
Simple IP project creation
Custom IP creation
IP creation using Vivado HLS
Block design creation in IP Integrator
Top level integration
This representative design will allow you to understand the recommended methodology for various Vivado sources
Notes: You must do the pre-work before attempting this lab.

## Slide 24
Learn how to set up a very small RTL project and demonstrate project creation with Tcl scripts, Make and dependencies
Lab Section 1 – Simple RTL Project

## Slide 25
Learn how to build an IP source using scripts and managed IP projects to be used as a remote source in a project
Lab Section 2 – Simple IP Project

## Slide 26
Learn how to package HDL as a custom IP for inclusion in IP Integrator
Lab Section 3 – Custom IP

## Slide 27
Learn how to build from C-based sources using scripts and packaging IP to be used in IP Integrator
Lab Section 4 – Vivado HLS

## Slide 28
Learn how to build a block design in IP Integrator to be used as a remote source
Lab Section 5 – IP Integrator

## Slide 29
Put it all together with a top level wrapper, including a System Generator IP as a remote source – compile and generate a bit stream
Lab Section 6 – Top Level Integration

## Slide 30: What you just accomplished
Now you can help your customers!
In the last hour you built a fresh Vivado project
  Set up directories
  Set up required scripts
  Set up a methodology for generating the design
Now you can iterate on the design and allow ‘make’ to help manage dependencies for you
You can check in and check out as you reach key milestones
Notes: The provided solution contains both approaches. The TCL script contains a switch to control which revision control approach is desired.

## Slide 31: Summary
There are two documented approaches to decide which files to manage
  Maximum flexibility / least rebuild time
  Minimum number managed files
A key is to use remote sources and not to manage the project directories
This lab used Git but the methodology can be applied to other revision control flows
Available documentation / materials coming soon!
  Chapter 2 in UG949, Quick Take Video, Lunch and Learn
Xilinx recommendation

## Slide 32
Q & A

## Slide 33
Thank You

## Slide 34
Backup

## Slide 35: Recommended directory structure
Root Dir
Work
HDL/TB
HLS
BD
IP/CIP
Scripts
XDC
DSP
All Sources are under revision control (dark red)
  Can be local disk space, or remote/shared location
  Read only or writeable depending on rev. control tool
Working directory is “ignored” – not under revision control (blue)
  You will create all your projects here – and reference remote sources (../)
  Build “Bottom Up” – copy intermediate deliverables for IP into rev ctrl

## Slide 36: IP under revision control
Use Standalone Manage IP
  Put the IP outside the project to be checked into revision control
  Choose a directory – normally at same level as working project
Check in the directory next to the managed_ip_project folder
  And everything below it (.xci, .dcp, .veo, . Xml)
  all subdirectories
Instantiate - Adding .xci as remote source
  Make sure “copy into project” option is not selected
  Must be fully generated, preferably w/ dcp

## Slide 37: IP Integrator under revision control
Create the block diagram in a remote directory
  Just like IP, and make sure it is fully generated
  Iterate until happy w/ BD
Check in entire directory
  And all subdirectories
Add .bd as a remote source in top project
  Read only is fine for implementation
  Must be fully generated

## Slide 38: Custom IP with IP Integrator
Build a small “managed ip” project for IP
Package it up to a directory
  Creates component.xml and xgui dirs
  Revision control this directory
To edit/update from an instantiated project:
  From within IPI BD select IP, choose Edit in IP Packager
  Creates a small temp directory and allows RTL edits and re-packaging
  Make sure you up revision each time
  Report_ip_status and upgrading should work like Xilinx IP
Important!

## Slide 39: System Generator under revision control
Build System Generator “Standalone”
  vs “composite” integration mode with Vivado
  Package SysGen Block like any other custom IP
  IP repo used in IPI or Managed IP project for RTL
  Make sure it is fully generated (RTL) with DCP (OOC)
Check it into revision control, like IP
  Entire directory, including all subdirs
Add .xci to top project as a remote source
  add_sources Tcl command, relative file path