## Slide 1
July 2015
Using Revision Control with Vivado
Notes: In this presentation we will cover methodology recommendations for using Vivado with revision control tools. You will get some specific information about how to work efficiently with revision control tools and have the opportunity to set up a project and work with some of the basic tasks.

## Slide 2
Overview of revision control (10 min)
Recommendations for Vivado (20 min)
Lab exercise using Git and Make (80 min)
Summary / Next Steps / Q&A (10 min)
Agenda
Notes: First there will be a brief review of why revision control methodology is important and why customers should be using it.
Then we will cover specifics of how to set up a Vivado project and what source files to manage within revision control.
Next we have a lab that will walk you through the process of setting up a project using Git as the revision control tool and a tool called “Make” to determine dependencies and control the flow of the build process to compile to a bit file. Git is chosen here as a popular option, but the concepts translate and are applicable to any revision control tool.
Finally we’ll summarize and discuss next steps.

## Slide 3: Why use revision control?
Automates critical management of development
  Milestones are “backed up”
  Can revert to previous milestone if necessary
  Changes are logged
Reduces compile times
  Dependency tracking – only build when inputs change
  Take advantage of parallelization – independent steps can run in parallel
Most customers use some form of revision control
The UltraFast Design Methodology Guide (UG949) recommends using revision control with Vivado Design Suite
Notes: Most FPGA developers use some form of revision control. These tools provide backup methodology that is far more rich than simply having saved copies of files. You define milestones and have the ability to revert and recover to these known good states of the design files and all changes to the files are logged and controlled.
The parallelization benefit comes from following the recommended methodology for revision control. This methodology focuses on dependency management, leverages bottom up design and allows the launching of OOC runs in parallel. There will be no runtime required to update things that don’t need to be updated.

## Slide 4: Which revision control systems do you use?
Notes: Here are 12 examples of revision control systems. This is not a comprehensive list. There is no single tool that represents a majority of our customer flows. Which one(s) do you use?

## Slide 5: Vivado revision control philosophy
Designed to be “friendly” to revision control
  No direct integration with specific tools
  Generally prefer ASCII-based internal files (XML project files)
  Tolerate hidden “dot” files and read-only sources “locked” in revision control
  Minimize file updates on opening projects and only write changes
Work with different use models
  GUI (IDE) vs non-GUI (TCL scripting)
  Project vs non-project flows
  Distributed vs centralized revision control repositories
Notes: It is clear that Vivado can’t be integrated with all of the revision control systems that customers may want to use. Therefore, Xilinx has a philosophy for Vivado Design Suite to make it as easy as possible for the customer to use Vivado with the revision control system of their choice.
Note that sources files are ASCII – even for data files. COE, BMM, etc are all ASCII.
Also note that there are quite a few binary files (bit files and others such as dcp). We do this when there is a clear advantage or engineering reason to do so. Often the reason is performance – a binary file is faster and more efficient to open and process data from than parsing ASCII.

## Slide 6: Recent improvements in Vivado
2015.1
  Only the .bd file is required to recreate a block design
  Compared to 2014.1 the average number of files per IP is about 1/3
  Increased / focused testing around recommended methodology
Updated Chapter 2 in the UltraFast DMG delivered June 8th!
Updated Revision Control Quick Take Video now live!
2015.3
  Introduction of core container – one file per IP
  Reduction of side files required by IP Integrator
  Further reduction in the number of files per IP
  New revision control tutorial available via DocNav
Notes: Here are some recent changes to Vivado that were instituted to improve the experience with working with revision control tools. For example in 2015.1 you can now choose to check in just the block diagram file (.bd) by itself and Vivado will recreate the design faithfully from the bd file. However, if you choose not to check in all the bd files as is recommended (we will cover this later) this bd file must be copied locally in to the project so all the files can be regenerated.
We’ve worked to drastically reduce the overall number of files in Vivado IP. On average the number of files has been reduced by 2/3. We’ve also increased our testing and prioritization of revision control related issues.
We have improved documentation, with a chapter focusing on rev. ctrl. Methodology in the ultrafast design methodology guide. We have updated the quick take video which provides a good overview of our methodology recommendations.
In 2015.3, we will have additional benefits with a project called “core container” that is effectively a zip archive of all the files in an IP so there will be a single self-contained file that needs to be managed with all needed sources inside. We will be further working to reduce file counts by providing common IP RTL libraries in a central location chosen by the use to enable pre-compilation and reduction of redundant files across IP and with multiply instantiated IP.

## Slide 7: Two documented revision control strategies
Chart: Revision Control Strategies
| 2 | 0.4
Flexibility | 2.7 | 0.8
Maximum Flexibility
  Option to use IP in future releases of Vivado without upgrading
  Shorter runtime to rebuild project
Minimum Files
  The least number of files to manage at the expense of flexibility and run time
Xilinx recommendation
Notes: Generally speaking there are 2 types of use cases that designers are concerned about. I’ll call these two strategies: 1) a Maximum flexibility and 2) minimum file strategies. Xilinx primary recommendation is described in the green box, and we advocate users to follow this approach which provides significant compile-time advantages and maximum “insulation” from being forced to upgrade IP when switching versions of Vivado. The key part of this is to generate IP, IPI subsystems, HLS fully and check them all into revision control and they will be used by Vivado unchanged – even in later versions of Vivado for P&R.
Some customers want to check in and manage an absolute minimum number of files necessary to recreate the design faithfully. That is a viable strategy – they just need to be aware that to do a full compilation they will have to regenerate all the IP and subystems which will take additional time. Furthermore, if they hit an issue or wish to take advantage of feature in a newer version of Vivado they will be forced to upgrade the IP to the version supported by the Vivado version. This can be a major complication and substantial verification burden.

## Slide 8: Overview of recommended directory structure
Manage different source types in separate remote directories
Use a “work” directory to compile the design and to create Vivado projects
Set up the Vivado project with remote sources from the various directories
  Elect to not copy them into the project
Either manage revisions from the remote sources area directly or use it as a local sandbox for the project
Notes: There are many viable ways or setting up a project directory structure. We want to provide an example that closely matches what many successful customers create to compile projects with revision control. For revision control the most important thing to mention is that whenever possible you should manage source types “remotely” which means they are not imported into the project directory structure. You should not place projects under revision control – treat them like intermediate “working” files and keep all your sources outside of the project.
So the directory structure has 2 types of folders: those that are under revision control and those that are not. We will call this a “work” directory and it is where you will build projects. Think of it as a local “sandbox” to play in where you can validate work prior to committing it to the actual check-in location.
You need to set up a project (using scripts or interactively with the GUI) in the working directory (outside rev ctrl) and utilize remote sources (make sure to deselect the “import into project” option in the GUI). The remote sources can point to the golden or master version of the repository or you can have an intermediate checkout version called a “staging area” where you will hold all your individual commitments prior to pushing them to all other users in the master or “golden” repository.
Typically you will have a folder for each type of source in the revision control area to hold: IP, IPI BDs, HLS, Scripts, Constraints, HDL sources etc…

## Slide 9: Project with sources under revision control
project_1.xpr
project_1.srcs
project_1.data
project_1.runs
constrs_1
sources_1
project_1.cache
sim_1
Remote Sources
HDL (Verilog/VHDL)
IPI BD (entire dir)
IP XCI (entire dir)
Sys Gen IP XCI (entire dir)
XDC Constraints
Tcl Scripts
Simulation Testbenches
COE/BMM/ELF
Notes: From a high level, this is how it would look. Only the items inside the gold clouds are managed by the revision control system. The xpr file itself is optional – you could also choose to have a Tcl script which will recreate the project. Note, that the files under the project directory structure are never under revision control.
If you choose to revision control the .xpr file instead of a script to create the project (Tcl script is primary recommendation) you need to understand that Vivado will try to recreate the project in the location of the xpr. So you must have write permission in the directory where Vivado will try to recreate the project. It’s best if you copy the xpr to the work directory (not under rev ctrl) to avoid the tendency to put projects under revision control.

## Slide 10: Maximum flexibility - Recommended files to manage
If using projects, manage just the .xpr file or the Tcl recreate script
  Use the write_project_tcl command to create a script to re-create the project
  Do not check in the project sub-directories
Use your own judgment on directory structures for RTL, XDC, etc.
For IP and IP Integrator sources, manage the entire directory tree
  Generated sources can be used in future Vivado releases
Notes: Going down one level of abstraction deeper, this is how it would look with the recommended flow that allows maximum flexibility.
The primary recommendation is to use TCL otherwise use the XPR. Make sure to test the XPR to make sure data is not missed and to check relative paths.
We recommend checking in the entire directory structure for IP, BD, etc. Trying to filter or limit the files will very likely corrupt the data and get you into trouble.

## Slide 11: Maximum flexibility - Recommended files to manage
Manage Vivado HLS source files, scripts, example projects, and packaged IP
Manage the entire System Generator directory for DSP sources
Manage Scripts and Docs as desired
For SDK, manage the .hdf file
Notes: Manage any handoff files.

## Slide 12: Minimum files - Recommended files to manage
If using projects, manage a Tcl script or just the .xpr file
  Use the write_project_tcl command to create a script to re-create the project or write a simple script manually
  Do not check in the project sub-directories
For IP, check in the .xci file only
  The .xci file can be used recreate the IP output products
  IP can only be recreated using the version of Vivado the IP was created with
For IP Integrator, check in the .BD file or the Tcl recreate script
  Use the write_bd_tcl command to create a script for the block design
Notes: If you must try to check in minimum data and recreate everything – you will need something to create the project (either the xpr file itself or a Tcl script to create the project). You will need the primary sources such as HDL files, constraints. And you will need the minimum files to recreate the IP which is the .xci file by itself. For IPI, you will need just the .bd file.
Note that Vivado needs write permission to create the content you didn’t check in to revision control – and it will try to do that in the same location as the xci/bd file. So if you elect minimum files, and check in only the xci/bd files your script for creating the top level project should copy them into the project – where they can be generated without running into issues with permission inside the repository.
Note that some IP have side files – Block Memory Generator, SysMon and FIR Compiler, for example.

## Slide 13: Minimum files – Recommended files to manage
Manage Vivado HLS source files, scripts, example projects, and packaged IP
Manage the entire System Generator directory for DSP sources
Manage Scripts and Docs as desired
For SDK, manage the .hdf file
Notes: Similar concepts with HLS source and custom packaged IP, and System Generator custom IP.
Scripts and other documentation collateral should also be managed in revision control.
For SDK the handoff is typically the .hdf file which is generated from Vivado. It, too should be checked into revision control.

## Slide 14: Knowledge check
What should be checked into a revision control system?
  BD
  IP
  Constraints
  Project directories
  Verilog sources
  VHDL sources
  All of the above
Which of the two documented approaches to revision control is the preferred approach that Xilinx recommends?
  Maximum flexibility or Minimum files
Notes: Quick quiz.
A: don’t ever check in project directories
A: We recommend the maximum flexibility approach because it insulates you from being forced to upgrade IP versions with Vivado versions and saves considerable runtime for compiles. It allows you to validate a configuration of IP and ensure there are no functional changes due to upgrades.

## Slide 15: Best practices for revision control
Create a Tcl script to recreate a project
  Write_project_tcl creates a “template” that you can use/modify
IP Integrator has write_bd_tcl
  Creates a Tcl script to recreate just the bd
  Highly version dependent – like the IP
Script check-in / check-out flow
Notes: Diff/merge tools from revision control
  Scripts to recursively check in/out directories
  Diff versions and staged changes
  Report changes between versions
  Back out and revert committed changes

## Slide 16
Git and Make Primer
Notes: Next we have a short “primer” on Git and Make – to give you an overview of common tools used in conjunction with revision control.
Git is a popular open source revision control system developed by Linus Torvalds (famous for Linux). It’s very fast and efficient.
Make is another open source utility that controls complex builds based on dependencies of files. It looks at time stamps of input sources and if they are later than output files it calls the step and re-runs all or a portion of the tool flow. It is very popular in software development environments.

## Slide 17: Git file life cycle
stage files
checkout
Git Rep.
Staged
Modified
Ignored
Files
Tracked Files
Unmodified
commit
edit files
add
remove
Notes: This picture describes the life cycle of files in the Git revision control nomenclature. Other tools have very similar concepts – we introduce these so we have a common set of terms.
You have files that are either tracked or untracked. Untracked files can be added to a configuration file so that the tools do not constantly report changes to these files.
Within tracked files you have levels of unmodified, modified, staged and the master git repository. You checkout files from the master repository to a local staging area and optionally edit and modify them. You typically collect these edits and test them together till you get to the point of a milestone or feature where you want to stage them – or group them in your local sandbox and test them. Committing is the process of pushing these changes up to the master git repository – ostensibly where the changes will propagate out to other users.
You can always revert or back out changes at these commit levels or even on individual file edits if you need to fix problems that get introduced.

## Slide 18: Working with source files in Git
To set up a new repository in an existing directory
  Initialize git (creates .git subirectory):
  Start tracking file changes:
  Create your initial “snapshot”:
Use the latest snapshot (possibly making local changes)
git init
git add *.v
git add *.vhd
find . –name “*” | xargs git add
git commit –m “Initial project version”
git clone \\full_path_to_master\myProject.git
Notes: Here are the most common commands in git. These are well documented in wikis and tutorials on the web.

## Slide 19: Working with source files in Git
Staging
  Query
  Discard any local changes and revert to last commit
  Report differences between staged and last commit
  Removing files from version tracking
  Ignore tracking (add files to ignore to .gitignore)
Branching and Merging
  Advanced workflows possible – following software design models
git status
git checkout
git diff
git rm foo.tcl
cat .gitignore

## Slide 20: Make – A brief primer on dependency management
Make is an open source tool to build things from source files
  Takes a “makefile” which describes how to build:
    Inputs to a compilation step
    Commands to execute
    Order of operations when there are multiple steps
    Steps that don’t need to be run are skipped (based on files and timestamps)
    Targets/dependencies are usually files on disk – commands generate files
Makefile structure
  target: dependencies …
    commands
    …
Documentation:
  http://www.gnu.org/software/make/manual/html_node/index.html
This is a Tab Character – don’t forget it!
Notes: If you’ve never used Make – here is a brief tutorial on what it is and how it works. There are also many tutorials on the web.
Make reads in a makefile which describes commands to execute (a target) which typically produces a file (or files) that indicate the step is complete. It also describes the input dependencies that the target depends upon. You write a target name then a colon and then list the dependencies one by one. Next line starts with a tab and then the command that is to be issued if the step is to be run. You can also run multiple commands – each one on a separate line starting with a tab. A blank line ends the target.
Make figures out the order of operations when targets depend on output products (files) from other targets. So you can build very complex compilation scripts – but only execute necessary steps when files change rather than rerunning everything all the time.
The most common mistake is to forget about the necessary tab characters in editing files.

## Slide 21: Standard conventions with Make
Calling “make” with a specific target – generates just that target
Calling “make” with no arguments – runs the first target
First target is “all”
  Builds everything in the project
  “All” is a phony target (no file on disk)
  Dependencies are all the inputs (and outputs of intermediate steps)
Last target is “clean”
  Deletes everything in the project dir (except Makefile)
  Always start clean
Notes: You can write very elaborate make files if you want – but you should start basic. There are a few common conventions – not required but so common you will see them everywhere. When you call “make” from a command line – it looks for a file named “Makefile” in the current directory and executes it. Typically you call it with an argument – the target you wish to have evaluated and run. If you don’t provide an argument it will run the first target.
By convention the first target is usually one called “all” which basically rolls all the steps up to build everything you want. Targets can be “phony” which means there isn’t really a file on disk to compare.
Another common target is a “clean” target which deletes everything in the current directory so you are starting from a clean location with no files left around as artefacts that could corrupt the tools.
You can name your Makefiles whatever you want – but these items are very typical.

## Slide 22
Lab Exercise
80 Minutes
Using Git and Make with Vivado

## Slide 23: Lab overview
This 80 minute lab exercise is broken down into 6 main sections
Simple RTL project creation
Simple IP project creation
Custom IP creation
IP creation using Vivado HLS
Block design creation in IP Integrator
Top level integration
This representative design will allow you to understand the recommended methodology for various Vivado sources
Notes: You should do the pre-work before attempting this lab. If you have not done the pre-work – go to the pre-work lab first to go over git and make –then come back to this lab.

## Slide 24
Learn how to set up a very small RTL project and demonstrate project creation with Tcl scripts, Make and dependencies
Lab Section 1 – Simple RTL Project

## Slide 25
Learn how to build an IP source using scripts and managed IP projects to be used as a remote source in a project
Lab Section 2 – Simple IP Project

## Slide 26
Learn how to package HDL as a custom IP for inclusion in IP Integrator
Lab Section 3 – Custom IP

## Slide 27
Learn how to build from C-based sources using scripts and packaging IP to be used in IP Integrator
Lab Section 4 – Vivado HLS

## Slide 28
Learn how to build a block design in IP Integrator to be used as a remote source
Lab Section 5 – IP Integrator

## Slide 29
Put it all together with a top level wrapper, including a System Generator IP as a remote source – compile and generate a bit stream
Lab Section 6 – Top Level Integration

## Slide 30: What you just accomplished
Now you can help your customers!
In the last hour you built a fresh Vivado project
  Set up directories
  Set up required scripts
  Set up a methodology for generating the design
Now you can iterate on the design and allow ‘make’ to help manage dependencies for you
You can check in and check out as you reach key milestones
Notes: The provided solution contains both approaches. The TCL script contains a switch to control which revision control approach is desired. It is controlled by an environment variable set in the Makefile called “reusegolden” When set to true it reuses the ip etc checked into the golden git repo – this matches the primary recommendation and the maximum flexibility use case. Change it to false and everything will be regenerated locally based on Tcl scripts. This is the minimum file use case.
You can iterate through this by editing files and calling make. When you are happy with a collection of changes you commit them and push into the repository.

## Slide 31: Summary
There are two documented approaches to decide which files to manage
  Maximum flexibility / least rebuild time
  Minimum number managed files
A key is to use remote sources and not to manage the project directories
This lab used Git but the methodology can be applied to other revision control flows
Available Now: Chapter 2 in UG949 Covers Revision Control
Xilinx recommendation
Notes: Today we gave you an overview of the Xilinx revision control best practices. We provide 2 approaches; one that offers maximum flexibility and best compile times. The second minimizes the number of files.
The most important part of the recommendation is to avoid the management of project directories with active projects. There are many intermediate files and Vivado needs to have control of them. Better to set up the project with remote sources that reside outside the project – this allows you to view and manage changes to your sources without sifting through diff logs of thousands and thousands of files.
We provided a lab with an example project showing common setup and workflow using git and make. These concepts are directly applicable to other revision control systems.
Chapter 2 in the Ultrafast Design Methodology Guide (UG949) has recently been published giving more details on these topics.
Good luck!

## Slide 32
Q & A

## Slide 33
Thank You