## Slide 1
Version Control Recommendations
June 2014
Vivado Design Suite
Notes: This presentation covers key recommendations in Vivado 2014.1 for customers.

## Slide 2: Agenda
Overview of Revision Control
Recommendations for Vivado Project Setup
6 Labs (1.5hrs)
Q&A

## Slide 3: General Revision Control Philosophy
Designed to be “Friendly” to Revision Control
  But we do not have direct integration with specific tools
  Generally Prefer ASCII-based internal files (xml project files)
  Tolerate read-only sources “locked” in revision control
  Tolerate hidden “dot” files inserted by version control tools
  Minimize file updates on opening projects and only write changes
Work with Different Use Models
  IDE vs non-GUI
  Project vs non-project
  Distributed vs Centralized Revision Control Tools
We do not recommend revision control on “active” projects
  Separate “sources” outside projects works best
  You save off a project – but easy to corrupt projects if you don’t get all files

## Slide 4: Helpers for Revision Control
Tcl script to recreate a project
  Write_project_tcl creates a “template” that you can use/modify
IP Integrator has write_bd_tcl
  Creates a tcl script to recreate just the bd
  Highly version dependent – like the ip
  Doesn’t currently work w/ remote sources
Make files with Tcl scripts
  Reproduce the project given input sources
  “Standalone” project file is an alternative for Tcl sources
Diff/Merge Tools from Revision control
  Scripts to recursively check in/out directories
  Diff versions and staged changes
  Report changes between versions
  Back out and revert committed changes

## Slide 5: Recommended Directory Structure
Project Dir
Work
HDL
XDC
HLS
BD
IP
Scripts
TB
CIP
DSP
All Sources are under revision control (dark red)
  Can be local disk space, or remote/shared location
  Read only or writeable depending on rev. control tool
Working directory is “ignored” – not under revision control
  You will create all your projects here – and reference remote sources (../)
  Build “Bottom Up” – copy intermediate deliverables for IP into rev ctrl

## Slide 6: Project with Sources Under Revision Control
project_1.xpr
project_1.srcs
project_1.data
project_1.runs
project_1.ioplanning
constrs_1
sources_1
project_1.cache
sim_1
Remote Sources
HDL (Verilog/VHDL)
IPI BD (entire dir)
IP XCI (entire dir)
Sys Gen SLX (entire dir)
XDC Constraints
Tcl Scripts
Sim Testbenches
COE/BMM/ELF

## Slide 7: IP Under Revision Control
Use Standalone Manage IP
  Put the IP outside the project to be checked into revision control
  Choose a directory – normally at same level as working project
Check in the directory next to the managed_ip_project folder
  And everything below it (.xci, .dcp, .veo, . xmlall subdirectories
Instantiate by adding .xci file as remote source
  Make sure “copy into project” option is not selected
  Must be fully generated, preferrably w/ dcp

## Slide 8: IP Integrator Under Revision Control
Create the block diagram in a remote directory
  Just like IP, and make sure it is fully generated
  Iterate until happy w/ BD
Check in entire directory
  And all subdirectories
Add .bd as a remote source in top project
  Read only is fine for implementation
  Must be fully generated

## Slide 9: Custom IP with IP Integrator
Build a small project just for IP
Package it up to a directory
  Creates component.xml and xgui dirs
  Revision control this directory
To edit/update from an instantiated project:
  From within IPI BD select IP, choose Edit in IP Packager
  Creates a small temp directory and allows RTL edits and re-packaging
  Make sure you up revision each time
  Report_ip_status and upgrading should work like Xilinx IP
Important!

## Slide 10: System Generator Under Revision Control
Build System Generator in a Standalone directory
  Like IP – separated from project
  Currently doesn’t support OOC
  Make sure it is fully generated (RTL)
Check it into revision control, like IP
  Entire directory, including subdirs
Add .slx to top project as a remote source
  add_sources Tcl command, relative file path
  No Matlab license required
  If you add via GUI, it will require a Matlab license and copy it locally

## Slide 11: Git Version Control File Life Cycle
stage files
checkout
Git Rep.
Staged
Modified
Ignored
Files
Tracked Files
Unmodified
commit
edit files
add
remove

## Slide 12: Working with Source Files (Git) – 1/2
Set Up New Repository in existing directory
  Initialize git (creates .git subirectory):
  Start Tracking file changes:
  Create your initial “snapshot”:
Use the latest snapshot (possibly making local changes)
git init
git add *.v
git add *.vhd
find . –name “*” | xargs git add
git commit –m “Initial project version”
git clone \\full_path_to_master\myProject.git

## Slide 13: Working with Source Files (Git as an Example) – 2/2
Staging
  Query
  Discard any local changes and revert to last commit
  Report differences between staged and last commit
  Removing files from version tracking
  Ignore tracking (add files to ignore to .gitignore)
Branching and Merging
  Advanced workflows possible – following software design models
git status
git checkout
git diff
git rm foo.tcl
cat .gitignore

## Slide 14: Make Brief primer on dependency management
Make is an open source tool to build things from source files
  Takes a “makefile” which describes how to build:
    Inputs to a compilation step
    Command to exectue
    Order of operations when there are many steps
    Steps that don’t need running are skipped (based on files and timestamps)
    Targets/dependencies are usually files on disk – commands generate files
Makefile Structure
  target: dependencies …
    commands
    …
Documentation:
  http://www.gnu.org/software/make/manual/html_node/index.html
This is a Tab Character – don’t forget it!

## Slide 15: Standard Conventions with Make
Call make with a specific target – generates just that target
Call make with no arguments – run the first target
First target is “all”
  Builds everything in the project
  “All” is a phony target (no file on disk)
  Dependencies are all the inputs (and outputs of intermdieate steps)
Last target is “clean”
  Deletes everything in the project dir (except Makefile)
  Always start clean

## Slide 16: Lab 1 – 10 minutes
Set up a new project with “ThreeFlop” RTL and XDC
Create a Makefile to call vivado with 3 targets:
  Setup creates a project with remote sources
  Compile opens the project and launches run to bitstream
  Clean – deletes everything except the Makefile
Use Git Commands to check in all sources, the Makefile, scripts
  git init
  git add
  git commit –m “initial project checkin”

## Slide 17: Lab 2 – 15 minutes
Create a Managed IP project for AXI_IIC
Using a script fully generate the IP with OOC flow
Check it into revision control
Iterate and change a customization option

## Slide 18: Lab 3 – 15 minutes
Create a Block diagram system with remote BD
Use write_bd_tcl to generate the BD
  Modify the tcl to create the bd “remote” to project
Add a bd generation target in makefile
Take the output of the generation (the remote bd) and check in to revision control
Iterate on a small change

## Slide 19: Lab 4 – 15 minutes
Package up custom IP RTL for IPI
  Using the bft RTL
Build a script to create a small project
  For packaging purposes
Take the output directory – check into revision control
Edit from within BD to change the RTL
  Check in changes into git
  Make sure and change version so update is automated

## Slide 20: Lab 5 – 15 minutes
Build HLS-Based IP from C++ Sources
Build a script and add a make target
Once generated, check in remote IP repository

## Slide 21: Lab 6 – 15 minutes
Given a System Generator DSP Subsystem
  Fully generated – no need to have Matlab licenses
Check in SysGen module into revision control
Modify setup script and Makefile to add in slx
Verify compilation takes sysgen HDL and links

## Slide 22: Summary
Revision Control Basics w/ Git and Make
  Build projects with controlled changes
  Back out revisions to specific milestones
Vivado Revision Control Methodology Recommendations
  RTL, IP, IPI, HLS IP, System Generator IP, Custom RTL IP
Hands On Labs
  Walk Through Project Setup, managing changes
Q & A